Test of the Unisep miniskimmer F 560 S

By the Norwegian Pollution Control Authority (SFT)

The day of test: Monday 14.10.1999

Temperature in the oil basin: 12 degree C

Test oil: Norne oil-with a high content of wax and sticky

Viscosity of the oil : 950 cp sek10

Volume of  test oil : 2000 litres (app 530 gallons)

The Unisep miniskimmer F560S is a small

compact skimmer with the engine –skimmer

-oil pump all mounted to a solid unit.

A special designed recovery bag can be adapted

directly to the outflow of the skimmer.

the skimmer is built to operate close to the

beach area.The F560S can easily be handled with

just one operator. Or where the water is a little bit

deeper-with a small boat-needs two persons.

The recovery bags is made for volumes  up to 600

litres.The oil pump is technical a small eccentric

pump, with  a max capacity of 3000 litres of oil

per hour (app108 cbf)                                                                                 TEST 1

Weight app 90 kg LxWxH =31x20x32 inches

Test no 1.

The skimmer is tested in calm water                                                            .

Measured capacity:1200 litres/hr (app 320 gallons)

Oil thickness in basin :1,2 inch.

Free water in the recovered oil(10 %

Test no 2 .

The skimmer is tested with a streaming water of 0,4 knots.

Oil thickness in the basin app. 2 inches

Measured capacity, 1750 litres/hr (app 790 gallons)

Free water in the recovered oil (10 %

Test no 3.

Same conditions as test no 2 but the skimmer is handled

with a crane and pushed against the light boom.

Measured capacity: 3000 litres/hr (app.790 gallons)

Free water in the recovered oil (10 %                                                          TEST 2 AND 3

Test no 4.

Same conditions as test 2 and 3.

Measuring the time to recovered  the 2000 litres of ,

oil stored in the basin: 1 hour

##### Oil thickness in basin: 2-3 inches

Disassemble and clean:

The F560S is very easy to disassemble

and clean.

The conclusion of  this test is that the UNISEP miniskimmer F560s is working very well with oil near the beach area.

The skimmer is not tested with polluted oil.

Arvid Reinertsen

# Text boxes

###### TESTRESULTS